## Slide 1: Introduction - Blynk - Firebase
1 / 43
NodeMCU
Eueung Mulyana https://eueung.github.io/012017/nodemcu
CodeLabs | Attribution-ShareAlike CC BY-SA

## Slide 2: NodeMCU DEVKIT V1.0 Firebase Version: 3.6.4 | Blynk Library v0.4.4 Arduino IDE 1.8.1

## Slide 3
Outline
Introduction
Using Arduino IDE
NodeMCU + Blynk
NodeMCU + Firebase

## Slide 4: Introduction

## Slide 6: NodeMCU
NodeMCU is a LUA based interactive firmware for Expressif ESP8622 Wi-Fi SoC, as well as an open source hardware board that includes a (CP2102/CH340/..) TTL to USBchip for programming and debugging, is breadboard-friendly, and can simply be powered via its micro USBport.
Ref: cnx-software

## Slide 7: NodeMCU Firmware + DevKits
NodeMCU is an eLua based firmware for the ESP8266 WiFi SOC from Espressif. The firmware is based on the Espressif NON-OS SDK and uses a file system based on spi¦s.
The NodeMCU firmware is a companion project to the popular NodeMCU DevKits, ready-made open-source development boards with ESP8266-12E chips.
The NodeMCU programming model is similar to that of Node.js, only in Lua. It is asynchronous and event-driven. Many functions, therefore, have parameters for callback functions.
Ref: NodeMCU Documentation

## Slide 8: 1. ESP-12E WiFi Module (16 GPIOs)
NodeMCU
DevKit v1.0
4 MB (32 Mb) Flash Storage
128 KB Memory
Micro USB(5V Power, Program, Debug)
2x15-Pin Headers (GPIOs, SPI, UART, ADC, Power)
Notes: Pins still at 3.3V!

## Slide 9: V1.0 Pin Map

## Slide 10: Arduino IDE

## Slide 11: Using Arduino IDE
http://arduino.esp8266.com/stable/package_esp8266com_index.json
Develop Sketches and Flash NodeMCU with Arduino IDE
(C-Style)!
Starting with 1.6.4, Arduino allows installation of third-party platform packages using Boards Manager.
Install Arduino IDE
Start Arduino and open Preferences window
Enter board URL into Additional BM URLs
Open Boards Manager and install esp8266
Select your NodeMCU board

## Slide 12: #2 | File | Preferences

## Slide 13: #3 | File | Preferences | BM URLs

## Slide 14: #4 | Tools | Board | Boards Manager

## Slide 15: #4 | esp8266

## Slide 16: #5 | Tools | Board | NodeMCU 1.0

## Slide 17: Blynk

## Slide 18: NodeMCU & Blynk
Using Arduino IDE
Configure Arduino IDE for NodeMCU (as before)
Install Blynk Library
Prepare/Configure Blynk App
Prepare the Board, Create the Sketch & Flash
Play the Project (Blynk App)!

## Slide 19
#2
Install Blynk Library
~/Arduino$ tree
.
|-- blank
| |-- blank.ino
|-- libraries
|-- readme.txt
2 directories, 2 files
#---------------------
~/Arduino$ tree -L 2
.
|-- blank
| |-- blank.ino
|-- libraries
| |-- readme.txt
| |-- Adafruit_NeoPixel
| |-- Blynk
| |-- BlynkESP8266_Lib
| |-- SimpleTimer
| |-- Time
| |-- TinyGSM
|-- tools
|-- BlynkUpdater
|-- BlynkUsbScript
11 directories, 2 files
URL: blynkkk/blynk-library

## Slide 20: #2 - Check

## Slide 21
#3 - Configure Blynk App

## Slide 22
#3 - Configure Blynk App

## Slide 23
#4 - Sketch

## Slide 24: #4 - Sketch - cf. Sketch Builder
24 / 43

## Slide 25: #5 - Play!

## Slide 26: Firebase

## Slide 27: NodeMCU & Firebase Using Arduino IDE
Configure Arduino IDE for NodeMCU (as before)
Install FirebaseArduino Library
Create a Firebase Project
Use Example Sketch FirebaseRoom_ESP8266
Prepare the Circuit & Flash
Play!

## Slide 28: #2 - Install FirebaseArduino

## Slide 29: #2 - Check

## Slide 30: #3 - Create Firebase Project

## Slide 31: #3 - Create Firebase Project : Host

## Slide 32: #3 - Create Firebase Project : DB Secret

## Slide 33
#4 - Example Sketch FirebaseRoom

## Slide 34
#4 - Example Sketch FirebaseRoom

## Slide 35: #5 - Prepare the Circuit

## Slide 36: #5 Prepare the Circuit
Vibration Motor (brrr): pin 5 (D1) - Blue LED Light Sensor (sunlight): pin A0 - Potentio Red LED (redlight): pin 12 (D6)
Button (pushbutton): pin 14 (D5)
Mini Fan (cooldown): pin 13 (D7) - Orange LED

## Slide 37
#include <ESP8266WiFi.h> #include <FirebaseArduino.h>
// Set these to run example.
#define FIREBASE_HOST "fbase-nodemcu.firebaseio.com"
#define FIREBASE_AUTH "g3mvizMBfpXpoSa446BXxPiiBduXFRhZUhgzMjDL" #define WIFI_SSID "lk8fm"
#define WIFI_PASSWORD "1234567890"
const int grovePowerPin = 15; const int vibratorPin = 5; const int lightSensorPin = A0; const int ledPin = 12;
const int buttonPin = 14; const int fanPin = 13;
void setup() {
Serial.begin(115200);
pinMode(grovePowerPin, OUTPUT); digitalWrite(grovePowerPin, HIGH);
pinMode(vibratorPin, OUTPUT); pinMode(lightSensorPin, INPUT); pinMode(ledPin, OUTPUT); pinMode(buttonPin, INPUT); pinMode(fanPin, OUTPUT);
// connect to wifi. WiFi.begin(WIFI_SSID, WIFI_PASSWORD);
Serial.print("connecting");
while (WiFi.status() != WL_CONNECTED) { Serial.print(".");
delay(500);
}
Serial.println(); Serial.print("connected: "); Serial.println(WiFi.localIP());
Firebase.begin(FIREBASE_HOST, FIREBASE_AUTH); Firebase.set("pushbutton", 0);
Firebase.set("sunlight", 0);
Firebase.set("redlight", 0);
37 / 43
FirebaseRoom_ESP8266

## Slide 38: #6 - Changing the Values from Firebase

## Slide 39: #6 - Changing the States from the Circuit

## Slide 40: Refs/Resources

## Slide 41: Refs/Resources
NodeMcu - An open-source firmware based on ESP8266 wifi-soc
nodemcu/nodemcu-devkit-v1.0
NodeMCU Documentation
esp8266/Arduino: ESP8266 core for Arduino
Getting Started - Blynk
Simple Led Control With Blynk and NodeMCU Esp8266 12E
FirebaseDemo_ESP8266 - firebase/firebase-arduino
NodeMCU is both a Breadboard-Friendly ESP8266 Wi-Fi Board and a LUA based Firmware
NodeMCU - Wikipedia

## Slide 42: More Refs/Resources
nodemcu/nodemcu-firmware: lua based interactive firmware for mcu like esp8266 NodeMCU custom builds
marcelstoer/nodemcu-build - Docker Hub
Comparison of ESP8266 NodeMCU development boards Comparison of tools and IDEs for NodeMCU

## Slide 43: END
43 / 43
Eueung Mulyana https://eueung.github.io/012017/nodemcu
CodeLabs | Attribution-ShareAlike CC BY-SA